## Slide 1: Estimation of Human Center of Mass and Inertial Parameters via Approximate Bayesian Inference
Robert C Grande and Dr. Doik Kim

## Slide 2: Problem Statement
Estimate Center of Mass (CoM) of human given joint angles from Kinect or Vicon camera
Estimate limb inertial parameters
  Limb mass
  Limb CoM location
Use low cost sensors and techniques available to general researchers

## Slide 3: Motivation
Rehabilitation
Fall Prediction

## Slide 4: Motivation
Realistic Simulation
Virtual Reality

## Slide 5: Motivation
Analysis of Human Dynamics
Humanoid Robot Teleoperation

## Slide 6: Limitations of Past Approaches
Direct measurement of inertial properties
  Using expensive equipment, specialized procedures
    Magnetic Resonance Imagery (MRI) [CK Cheng 2000]
    Stereoprogrammatic [McConville 1980]
    Motion Capture and Force plates [Venture 2008]
  Post mortem measurements
    Divides corpse into segments and performs analysis directly
Indirect estimation using inverse kinematics models
  Limited prediction capabilities
    Returns CoM prediction, not limb properties [González 2012]
  Require expensive setup: Motion Capture and Force plates
    Not guaranteed to return feasible parameters, i.e. negative mass
  Our Approach

## Slide 7: Approach Overview
Collect joint and CoM measurements using Kinect and Wii Balance Board
Use inverse kinematics equations to determine limb properties

## Slide 8: Approach Overview
Problem:
  Wii and Kinect cannot collect dynamic data
  Impossible to estimate intertial parameters from static data alone
Solution:
  Formulate problem in probabilistic manner
  Use mass distribution data from medical literature as prior distribution
  Solve for Maximum A Posteriori (MAP) solution using approximate Bayesian inference

## Slide 9: Contributions
Introduce novel method for estimating the CoM and inertial parameters of a human operator
  Uses inexpensive and readily available equipment
    Wii Balance Board
    Kinect Camera
  Returns inertial parameter estimates as well as CoM predictions
  Returns feasible assignments for inertial parameters
  Utilizes wealth of past knowledge from the medical literature.
  Outperforms state of the art algorithms in CoM prediction

## Slide 10: Model

## Slide 11: Idea: Least Squares

## Slide 12: Problem: Unobservability
Redundant Columns: Observability Problem

## Slide 13: Idea: Bayesian Inference
Formulate in probabilistic framework: Bayesian Inference
  Given prior probability density function (pdf) p(theta)
    Designed by experimenter using medical literature
  Observation likelihood pdf p(y|theta): measurement model
  Desired: posterior pdf
  Z is normalization factor so p(theta|y) integrates to 1
  Intractable to compute in practice

## Slide 14: Idea: Bayesian Inference

## Slide 15: Method 1: Markov Chain Monte Carlo (MCMC)
Idea: Can’t evaluate p(theta|y) directly, but can we draw samples from p(theta|y)? Can then evaluate function proportional to p(theta|y)
Can’t draw samples from p(theta|y), but can we sample from another distribution and alter the result to look like p(theta|y)?
Rejection Sampling

## Slide 16: Method 1: Markov Chain Monte Carlo (MCMC)
MCMC: Adaptive Rejection sampling
Create a random walk: Accept new samples proportional to prob of new sample divided by prob of old sample

## Slide 17: Markov Chain Monte Carlo (MCMC)

## Slide 18: Method 2: Particle Filter
MCMC works well for batch data, but how about online methods?
  Can offer user feedback to encourage exploration [González 2013]
Idea: approximate continuous function using discrete set of basis functions
  Normalization becomes trivial sum
  Updates reduce to simple multiplicative updates of weights
  MAP calculation becomes search over discrete objects

## Slide 19: Particle Filter

## Slide 20: Particle Filter

## Slide 21: Particle Filter

## Slide 22: Prior Formulation

## Slide 23: Results: CoM Prediction: MCMC

## Slide 24: Results: CoM Prediction: Particle Filter

## Slide 25: Results: CoM Prediction: Gonzalez et. al

## Slide 26: Results: Inertial Properties

## Slide 27: Conclusions
Introduced novel method for determining inertial parameters of human
  Used low cost Wii Balance Board and Kinect Camera
  Used Bayesian inference and distributional data from the medical literature
    Solves problem of observability
    Adds regularization to the problem
  Better CoM prediction accuracy than state of the art algorithms
  Realistic estimates of inertial parameters